## Slide 1
Python and GUI Implementation for Internal Optimization and Increased Usability of in vivo Glucose Sensing System
This material is based upon work supported
by the National Science Foundation
under Grant No. EEC-0540832.
Kathryn DiPippo1,2, Alex Werth1, Michelle Zhang1,3, Phillip Heucke1,4, Jessica Doyle1,5, Claire Gmachl1
www.mirthecenter.org
1 – Princeton University Department of Electrical Engineering, Princeton, NJ, 08540, USA
2 – Permanent Address: Rensselaer Polytechnic Institute, Troy, NY, 12180, USA
3 – Permanent Address: Smith College, Northampton, MA, 01063, USA
Industry / Practitioner Collaborators: Daylight Solutions Inc. Zurich Instruments
4 – Permanent Address: Bucknell University, Lewisberg, PA, 17837, USA
5 – Permanent Address: Hunterdon Central Regional High School, Flemington, NJ, 08822, USA
email: dipippo@princeton.edu / dipipk@rpi.edu
Introduction
GUI Design
Setup and Method
Code Conversion and Examination
Future Plans
CLINICAL TRIALS VERSION
IN-LAB, “SOLUTIONS" VERSION
The GUI itself was designed to feature two different modes: one for use with clinical trials and one for use in the lab.
More simplified design
Data stored in text files for later analysis regarding the patient
- Designed for more variable
manipulation
- Allows for altering signal
processing values
- Options to alter the data
processing steps
Michelle Zhang designed and implemented a real-time analysis calculation code, which once completed for Python will be integrated into the GUI code to display an estimate value.
All dates are taken using the Python time library, meaning they are automatically printed in entry boxes at startup.
Dummy loading bar that lasts for 10 seconds while data is being taken.
“Load Data” runs the dummy loading bar (above). “BEGIN SENSING” takes the data. These are to be pressed simultaneously.
Opens folder dialogue to select where the data will be saved and retrieved.
“Exit” safely quits the application.
- Diabetes afflicts 9.3% of the entire
United States population, remains “the 7th leading cause of death”, by to 2014 statistics
- Diabetics must monitor their blood glucose
levels to ensure they stay healthy and
administer insulin if needed
- Goal is to enhance mid-infrared Quantum
Cascade Laser based non-invasive glucose
sensor to provide an alternative to obtaining
direct blood samples multiple times per day
to measure glucose levels.
Photo Credit to: https://loonylabs.files.wordpress.com/2014/08/blood-sugar.jpg?w=590&h=392
We would like to acknowledge the Wendy and Eric Schmidt Foundation, the National Science Foundation (Grant No. EEC – 0540832), and Daylight Solutions, Inc. in San Diego, CA for their
vital contributions to this research.
Schematic of the sensor design consisting of a QCL, gold coated integrating sphere with three ports, and a TE-cooled detector.
QCL
  EC-QCL produced by Daylight Solutions, Inc.
  Light pulsed at 55 kHz with duty cycle of 1%
  Scanned between 1020–1220 cm-1
Integrating Sphere
  Gold coated
  Sphere diameter of 7.62 cm
  Port diameters: Input -> 3 cm, sample -> 2.5 cm, output -> 1.5 cm
Detector
  TE cooled MCT detector
  Mobile
  Specific detectivity of 109
Spectral Analysis
  Partial least squares regression
  Accuracy increases with number of calibrations
  Depends on linearly proportional metrics
  - GUI started up and populated with data
  - Number of spectral runs are taken
  - Various statistical analyses applied:
  - Wavelet transform
  - Savitzky-Golay Filtering with Differentiation
  - Machine Learning Prediction Algorithm
  - Final predicted glucose concentration
  obtained
The backscattered light from human wrist is collected by an integrating sphere and directed into a TE-cooled detector. The signal from the detector is used to predict the concentration of glucose in the subject’s blood.
- Optimize and miniaturize the three key components and place in mobile
case for clinical trials to increase the throughput and mobility.
- Integrate the code for real-time data analysis into GUI to produce the
scattering data along with the prediction in minimal time
- Soon, we hope to bring our mobile sensor into clinical trials at
diagnostic labs to obtain datasets from diabetic users.
Current Python code in use for the clinical GUI. It measures less than 400 lines and performs all the functions of the prior long MatLab Code.
Prior MatLab code contained functions compatible with currently defunct systems and was not properly maintained with comments and structure
Rewritten code in Python allowed for:
prior defunct functions to be removed
Structure within the code to be established with comments
additional libraries associated with python to be utilized (ex. Tkinter GUI library)
MatLab files needed prior to conversion
Python files needed after conversion
Directory related functions
Function that plots graph of input data
Zurich Instruments data polling function; reads in scattering signal from detector
Libraries and variable initialization
Data collection function
Dummy loading bar function
GUI layout function (Clinical version shown)
MAIN